Lab Report on Network Topology Creation with RIP and OSPF
Student Name: VISHWANATH PRADAPSINGH G
Course: B.TECH CSE AIML A
REG NO: RA2211026050029
Date: 21.10.24

Introduction
This report details the setup and configuration of a network topology using the Routing Information Protocol (RIP) and Open Shortest Path First (OSPF) in Cisco Packet Tracer. The objective was to create two local area networks (LANs) that communicate with each other using different routing protocols.

Network Topology Design
The network topology comprises two LANs connected via two routers. The topology includes:
Devices Used:
2 Routers: Router1 and Router2
2 Switches: Switch1 (for LAN1) and Switch2 (for LAN2)
12 PCs: 6 in LAN1 and 6 in LAN2
LAN1 Configuration
Subnet: 192.168.1.0/24
PC_001: 192.168.1.1
PC_002: 192.168.1.2
PC_003: 192.168.1.3
PC_004: 192.168.1.4
PC_005: 192.168.1.5
PC_006: 192.168.1.6
LAN2 Configuration
Subnet: 192.168.2.0/24
PC_007: 192.168.2.1
PC_008: 192.168.2.2
PC_009: 192.168.2.3
PC_010: 192.168.2.4
PC_011: 192.168.2.5
PC_012: 192.168.2.6

Routing Protocol Configuration
Router1 Configuration (RIP)
Access the CLI of Router1:
enable
configure terminal
router rip
version 1
network 192.168.1.0
network 192.168.2.0
Router2 Configuration (OSPF)
Access the CLI of Router2:
enable
configure terminal
router ospf 1
network 192.168.2.0 0.0.0.255 area 0
These configurations enable Router1 to use RIP for routing and Router2 to use OSPF, facilitating communication between the two LANs.
Message Transmission Simulation
To verify successful communication between LAN1 and LAN2, I conducted a ping test. The test was executed from PC_001 in LAN1 to PC_007 in LAN2. The command used was:
ping 192.168.2.1

configuration of router 1:

configuration of router 2:

Conclusion
In conclusion, the lab exercise successfully demonstrated the creation of a network topology using RIP and OSPF routing protocols